## Slide 1: Introduction to Parallel Computing
Parallel MODFLOW Training Class, July 13-14, 2023, Lakewood, CO
Notes: Why parallel?
Different forms of parallelism, which one for MODFLOW 6?
Theoretical expectations on performance?

## Slide 2
Large domain size
Complex calculations
Interaction of small and large scales
Computational Challenges
Why would you need a supercomputer?
Towards national/continental scale hydrologic models
Not there yet, why?
Notes: Examples of large scale problems, challenging and typically solved on supercomputers
Large-scale (national/continental) Integrated Hydrologic Models present similar challenges
Why lagging? Perhaps due to large parameter uncertainties of the simulated domain? So a lot of attention has gone to (distributed) Parameter Estimation

## Slide 3
Gordon Moore (1929-2023)
from Electronics, pp. 114–117, April 19, 1965

## Slide 4: Moore’s Law: the end of it…
Why haven’t clock speeds increased, even though transistors have continued to shrink?
Notes: Why haven’t clock speeds increased, even though transistors have continued to shrink?
Dennard Scaling postulated that as transistors get smaller their power density stays constant, so that the power use stays in proportion with area. This allowed CPU manufacturers to raise clock frequencies from one generation to the next without significantly increasing overall circuit power consumption. But there was a limit to how long this would last. Smaller devices with thinner dielectrics and shorter channels are more prone to leakage.

## Slide 5: Overnight Law
“Every new generation of models we have more data, demand higher precision, increase the complexity of our calculations…”
“… yet with the new laptops, we can still run our models overnight and present results in the morning…”
No more free lunch, at least not without extra work to have your software benefit from
the increase of the nr. of cores in a PC
novel accelerator hardware (GPU, TPU, FPGA, QC)

## Slide 6: Parallel Computing
Bit level
Instruction level
Data parallelism
Task parallelism
Our strategy: Data Parallelism,
for speed and memory distribution
Notes: So if you want to speed up, you go parallel!

## Slide 7: Parallel Computing
Notes: So if you want to speed up, you go parallel!

## Slide 8: Parallel Computing Communication
Efficient communication key to parallel performance
Bandwidth, Latency, Message size determine Idle Time
Optimize?
  Maximize throughput
  Reduce latency
  Minimize message size
time
throughput
SEND
time
RECV
Latency
∝ Bandwidth
throughput
∝ Message Size
Idle Time

## Slide 9: Parallel Computing Communication Efficiency
Bandwidth and latency are properties of the hardware
Developer can reduce latency by bundling messages
Modeler can reduce message size by splitting a domain into subdomains in an optimal way:
How to split a model with 4 layers, 200 rows, 1000 columns into 4 subdomains?
  Over layers: up to 400k remote cell connections in a subdomain
  Over rows: 8k
  Over columns: 1.6k

## Slide 10: Parallel Computing Message Passing Interface
MPI: Message Passing Interface for exchanging data
Standardized and portable
Different implementations:
  MPICH, OpenMPI, Intel, MS, and e.g. Cray-MPICH
Messages can be routed over LAN (PCs, Clusters)
Messages routed over fast interconnect, e.g. Infiniband/Omnipath/… (Supercomputers)
Latency can vary from ms to μs!
Standard:
Infiniband:

## Slide 11: Limit on Speedup
Further division of the work (i.e. smaller domains, increase in processor cores) increases communication overhead
Put differently: how large can you make your model?!
Amdahl’s law:
Speedup ≤
with p = parallel portion
Notes: How much faster can you get?

## Slide 12: A note on Speedup
Should I use Algorithm 1 or Algorithm 2?
How about now?
Figure by W. Gropp
Figure by W. Gropp
A modeler cares about Time to Solution!
Notes: You can always improve the scaling by destroying performance per processor and/or by choosing a very computationally expensive algorithm

## Slide 13: Limit on Memory Bandwidth
π = Peak Performance
β = Peak Bandwidth
I = Arithmetic Intensity
Roofline Model:
24 Bytes (2 load, 1 store)
2 FLOPS, 1 ADD and 1 MUL
which gives 1/12 FLOPS/Byte
DO i = 1, N
y(i) = a*x(i) + y(i)
END DO
Example: DAXPY
CG method: OI ≈ 0.4
i.e., a higher peak performance
will not lead to a shorter run time…

## Slide 14: Memory Bandwidth Bound
nr. of processors
speedup
ideal
= 4 ppn ($$$$)
= 8 ppn ($$)
= 16 ppn ($)

## Slide 15
Questions?

## Slide 16: Parallel MODFLOW 6: Expectations
Reduce simulation run time
Deal with increasing model size
  National, Continental scale
  Integrated, Multi-process
Increase size of models…
Distribution of memory load
  Fit really large problems on a machine

## Slide 17: Amdahl Example

## Slide 18: Roofline